## Slide 1
VA DIVISION A • 2025–2026
Bridge Building
Official Study Guide • 2025–2026 Season
Official Rules
Scoring Formula
Truss Types
Tension vs Compression
Build Strategy
Competition Tips

## Slide 2
📋 Event Overview
Rules
BRIDGE BUILDING • VA Division A • 1 of 8
Build the TALLEST truss bridge from straws and tape to span a 30 cm gap — hold a 300g or 500g mass for 30 seconds. Score = Height + Assessment. Max = 100 points.
Materials:
30 paper straws (~20 cm each), 1 meter of 2.54 cm masking tape. Nothing else.
Span:
Bridge must span exactly 30.0 cm between the two provided support structures.
Min Width:
Bridge must be at least 10.0 cm wide at center (outside edge to outside edge).
Loading Block:
5×5×0.6 cm block (20g) placed on the top chord at center before the test mass.
Masses:
Hold 300g for 30s for base score. Hold 500g for 30s for 1.2× height bonus.
Clear Path:
No internal cross-members that would block the 5×5 cm block from passing through.
Safety:
ANSI Z87+ impact-rated glasses required. Bring your own — not provided at event.
Written Test:
Concurrent written assessment on bridge types and forces during the 25-minute build.

## Slide 3
🏅 Official Scoring Formula
Scoring
BRIDGE BUILDING • VA Division A • 2 of 8
Team Score = 0.5 × (THS ÷ CHS) + 0.5 × (TAS ÷ CAS) × multipliers • Maximum = 1.0 (normalized)
Term
Meaning
Source/Impact
THS — Team Height Score
Your bridge's measured center height in mm
From measurement
CHS — Competition Height Score
Tallest bridge among all competing teams
Divides THS
TAS — Team Assessment Score
Your written test score
From assessment
CAS — Competition Assessment Score
Highest assessment score among all teams
Divides TAS
Bonus ×1.2
500g mass held for 30s → height score × 1.2
Best outcome
Penalty ×0.5
Width < 10 cm OR loading block can't pass through
Design fault
Height = 0
Bridge fails to span the 30 cm gap
Zero score
Tiebreaker 1
Most unused complete straws remaining
Save material!
Tiebreaker 2
Time to failure in 500g test (longer = better)
Secondary
Example: Your height 320mm, best=400mm → THS/CHS=0.80. Your test 8/10, best=10 → TAS/CAS=0.80. Score = 0.5×0.80 + 0.5×0.80 = 0.80. With 500g bonus: 0.40 + 0.5×0.80 = 0.84

## Slide 4
🔩 Truss Bridge Components
Components
BRIDGE BUILDING • VA Division A • 3 of 8
A truss bridge carries loads through a framework of triangles. Every component has a specific role — and knowing whether each member carries tension or compression is tested on the written assessment.
TOP CHORD
Upper horizontal member running the bridge's full length.
Force: Usually in COMPRESSION under a center load.
★ Most likely to buckle — bundle straws or slide one inside another for strength.
BOTTOM CHORD
Lower horizontal member at deck level.
Force: Usually in TENSION — being pulled apart.
★ Tape joints well — tension failures happen at connections, not mid-member.
VERTICALS
Members perpendicular to the chords.
Force: Compression (Howe/Warren) or Tension (Pratt) depending on truss type.
★ In Pratt truss: verticals carry compression. In Howe: verticals carry tension.
DIAGONALS
Angled members connecting top and bottom chords.
Force: Pratt = tension. Howe = compression. Warren = alternates.
★ Direction of diagonals defines the truss type — memorize the difference for the test!
JOINTS / NODES
Connection points where members meet.
Force: Forces assumed to act only at joints in ideal truss analysis.
★ Most real failures happen at joints. Tape each joint from multiple directions.
LOADING BLOCK AREA
5×5 cm block sits on top chord at center.
Force: Concentrated load applies maximum bending moment at bridge center.
★ Reinforce the top chord near center — this is where failure usually begins.

## Slide 5
🌉 Types of Truss Bridges
Truss Types
BRIDGE BUILDING • VA Division A • 4 of 8
PRATT TRUSS
Diagonals → tension
Verticals → compression
Most common design. Diagonals slope TOWARD the center.
★ Diagonal direction: lean inward, toward center.
HOWE TRUSS
Diagonals → compression
Verticals → tension
Opposite of Pratt. Diagonals slope AWAY from the center.
★ Diagonal direction: lean outward, away from center.
WARREN TRUSS
Alternates tension/compression
No verticals (basic form)
Equilateral triangles with alternating diagonal directions. Simple and efficient.
★ No verticals in basic Warren — only alternating diagonals.
PARKER TRUSS
Like Pratt (tension)
Like Pratt (compression)
Pratt variant with a curved top chord — deeper at center where moments are highest.
★ Also called 'camelback truss' for its arched profile.
BOWSTRING TRUSS
N/A — arched top chord
Varies
Arched top chord (in compression like a bow) with straight bottom chord in tension.
★ Bottom chord acts like a bowstring. The arch carries loads by compression.
K-TRUSS
Two diagonals meet each vertical at mid-height
Central vertical
Named for K-shaped panels. Used for tall long-span bridges.
★ Each panel looks like the letter K — one diagonal up, one diagonal down.

## Slide 6
⚡ Tension, Compression & Force Analysis
Forces
BRIDGE BUILDING • VA Division A • 5 of 8
TENSION
◆ Forces PULL the member apart (stretching)
◆ Member elongates under tension
◆ Bottom chord of a loaded bridge = tension
◆ Diagonal members in Pratt truss = tension
◆ Straw bridges fail in tension at joints — tape carefully!
◆ Tension members can be made from thinner material
◆ String, wire, and rubber bands resist tension well
COMPRESSION
◆ Forces PUSH the member together (squeezing)
◆ Member shortens or BUCKLES under compression
◆ Top chord of a loaded bridge = compression
◆ Diagonal members in Howe truss = compression
◆ Straw bridges fail in compression by buckling!
◆ Bundle straws or slide one inside another to resist
◆ Short, fat columns resist buckling better than long thin ones
ANALYSIS METHODS
◆ Method of Joints: apply ΣFx=0 and ΣFy=0 at each joint
◆ Start at a joint with only 2 unknown forces
◆ Unknown = member force (+ tension, − compression)
◆ Method of Sections: cut through 3 members max
◆ Take equilibrium of one half to find cut member forces
◆ Useful when only a few members need analysis
◆ Both methods assume pin (hinge) joints — no bending at joints

## Slide 7
🔧 Build Strategy — 25-Minute Session
Strategy
BRIDGE BUILDING • VA Division A • 6 of 8
1
Design first (0–3 min)
Sketch your Warren or Pratt truss. Count straws: ~10 for bottom chord + verticals, ~8 for top chord, ~8 for diagonals, 4 reserve. Set target height (aim high!).
2
Assign roles
One student takes the written test. The other leads the build. Both must know the 10cm width requirement and know not to block the 5×5 loading block path.
3
Build one truss side first (3–12 min)
Lay straws flat to form one side of the truss. Connect diagonals before lifting. Let tape set by pressing each joint firmly. Check width is ≥10 cm.
4
Build second side + cross-bracing (12–20 min)
Mirror the first side. Add cross-bracing connecting both sides — X-patterns on the faces resist racking. Cross-bracing also increases height if done vertically.
5
Reinforce and measure (20–24 min)
Measure center height to the nearest mm. Reinforce any loose joints. Check loading block path is clear. Measure width one final time — must be ≥10 cm!
6
Save your straws (ongoing)
Unused complete straws are Tiebreaker 1. Do NOT cut straws unless necessary. Every whole straw saved is a potential tiebreaker win.

## Slide 8
📖 Key Vocabulary & Famous Bridges
Vocab
BRIDGE BUILDING • VA Division A • 7 of 8
Truss:
Framework of interconnected triangles that forms the load-bearing structure of a bridge
Chord:
The top or bottom horizontal member running the length of a truss
Diagonal:
Angled member connecting the top and bottom chords
Vertical:
Perpendicular member connecting the top and bottom chords
Tension:
Force that pulls a member apart — member elongates
Compression:
Force that squeezes a member together — member shortens or buckles
Buckling:
When a slender compression member suddenly bends sideways and fails
Method of Joints:
Analyzes truss forces using ΣFx=0, ΣFy=0 at each joint
Through Truss:
Load passes through the truss (between top and bottom chord)
Deck Truss:
Load travels on top of the truss (on the top chord)
Pratt Truss:
Diagonals in tension, verticals in compression. Diagonals lean inward.
Howe Truss:
Diagonals in compression, verticals in tension. Opposite of Pratt.
Warren Truss:
Alternating diagonals, no verticals in basic form
Bowstring Truss:
Arched top chord (compression) with straight tension bottom chord
THS:
Team Height Score — your bridge's center height in mm
CHS:
Competition Height Score — tallest bridge among all teams