## Slide 1
VA DIVISION A • GRADES 3–4 • 2025–2026
Bungee Egg Drop
Competition Project Slides
Official Rules
Scoring Formula
Artificial Horizon
Bungee Design
Energy Physics
Competition Tips
Design a rubber band bungee system to stop a raw egg as close as possible to the Artificial Horizon without going past it.

## Slide 2
📋 Event at a Glance
Bungee Egg Drop • Slide 1 of 10 • VA Division A 2025–2026
2
Students per team
25
Min build + test
2
Drops allowed
50cm
Tape provided
4
Band sizes
100 pts
Max score
GOAL: Connect rubber bands into a bungee cord. Drop an egg (sealed in a plastic bag) from a two-story railing. Stop it as close to ZERO on the Artificial Horizon chart as possible — without going PAST zero.
Written test:
Taken SIMULTANEOUSLY during the 25-minute build phase. Topics: Conservation of Energy, GPE, KE, EPE.
Materials:
Rubber bands (#19/#33/#64/#117B), 50cm masking tape, 1 large egg, 1 plastic bag.
Tape restriction:
Tape may ONLY attach bungee to bag. Cannot support or strengthen the egg or bag.
Egg inspection:
Egg rolled on paper towel after drop. Any wet area = broken = Tier 2 (−20%).
Two drops:
May adjust bungee between drops. Best drop score is used in scoring.
Estimate:
Must announce estimated stop distance to supervisor. This is Tiebreaker 1!
Safety:
ANSI Z87 D3 splash/droplet GOGGLES (full seal) required. NOT just impact glasses.
Tier 3:
Did not follow Spirit of the Problem = −30% penalty.

## Slide 3
🏅 Official Scoring Formula
Scoring
Bungee Egg Drop • Slide 2 of 10 • VA Division A 2025–2026
Final Score (FS) = Assessment Score (AS) + max(Drop Score 1, Drop Score 2) • Max = 100 points
Term
Formula
Notes
Assessment (AS)
50 × (your Raw Assessment Score ÷ best RAS among all teams)
Max 50 pts
Drop Score 1 (DS1)
50 × (TDD − DD1) ÷ max(TDD − DD for all teams)
Closer = higher
Drop Score 2 (DS2)
50 × (TDD − DD2) ÷ max(TDD − DD for all teams)
Best drop used
TDD (Target Drop Distance)
Announced distance from railing to Artificial Horizon. Minimum = 200 cm.
Set at event start
DD (Drop Distance)
200cm if egg passes below horizon; else distance from horizon to lowest egg point.
From slow-mo video
Tiebreaker 1
Smallest difference between your ESTIMATED and ACTUAL drop distance.
Announce carefully!
Tiebreaker 2
Correct answers on selected written assessment questions.
Know your formulas
★ Example: TDD=400cm. RAS=6, best=9 → AS=33.33. 2nd drop DD=13cm, best DD=7cm → DS2=(400−13)÷(400−7)×50=49.24. Final Score = 82.57

## Slide 4
📊 The Artificial Horizon — Explained
Horizon
Bungee Egg Drop • Slide 3 of 10 • VA Division A 2025–2026
ARTIFICIAL HORIZON CHART
+100cm
Too short — cord too stiff
+50cm
Good — close to target
0 = Horizon
PERFECT — maximum score
−50cm
Broke through — 200cm penalty
−100cm
Floor — DD = 200cm (worst)
The chart is mounted on a wall. Supervisor records the lowest point the egg reaches in slow-motion video.
1
Attach bungee to Retaining Hook
The END opposite the egg attaches to the hook. Rubber bands hang loose over front of platform.
2
Hold egg vertical at platform edge
Hold the egg (in bag) at the end of the jump platform in a VERTICAL position. Any holding style is fine.
3
Countdown and open hand
"3, 2, 1, drop" — OPEN hand. DO NOT push the egg. Any upward movement = violation.
4
Adjust between drops
Went past zero? Add shorter/stiffer bands. Stopped too high? Add longer bands or remove short ones.
5
Egg inspection
Remove egg from bag. Roll on paper towel. Any wet spot = broken = Tier 2. Cracks without leaking = OK.
Supervisor records: estimate, slow-mo video, distance to nearest 1cm, written assessment scores.

## Slide 5
🔗 Bungee Design Strategy
Design
Bungee Egg Drop • Slide 4 of 10 • VA Division A 2025–2026
RUBBER BAND SIZES
◆ #19 — shortest, stiffest
◆ #33 — medium length/stiffness
◆ #64 — longer, softer
◆ #117B — longest, most stretch
◆ SERIES (end-to-end): longer cord, more total stretch
◆ PARALLEL (side-by-side): stiffer cord, less stretch per force
◆ Cut bands to make them shorter and stiffer
CALIBRATING YOUR BUNGEE
◆ At start: supervisor announces TDD (target distance)
◆ Calculate: bungee length + max stretch = approx TDD
◆ Test on floor: hang egg from fixed point, measure stretch
◆ Stopped short? Add longer bands or remove short ones
◆ Went past zero? Add shorter/stiffer bands
◆ First drop = data. Adjust. Second drop = score attempt.
◆ Write your estimate carefully — Tiebreaker 1!
ENERGY FORMULAS FOR THE TEST
◆ GPE = m × g × h (gravity PE)
◆ KE = ½ × m × v² (kinetic energy)
◆ EPE = ½ × k × x² (elastic PE)
◆ At top: ALL energy is GPE
◆ Falling freely: GPE → KE
◆ Bands stretching: KE → EPE
◆ Lowest point: ALL energy is EPE

## Slide 6
🏆 Competition Tips — How to Win
Tips
Bungee Egg Drop • Slide 5 of 10 • VA Division A 2025–2026
01
D3 goggles — not just glasses
Full-seal ANSI Z87 D3 (splash-rated) goggles are required. Regular impact glasses are NOT sufficient. Check "D3" on the label. Without them: no-show score.
02
Seal the egg completely
Seal the egg fully in the plastic bag before every drop. Any leakage after drop = broken = Tier 2 (−20%). Practice sealing quickly.
03
Know your estimate
Tiebreaker 1 is the closest estimate to actual drop distance. Time your test drops with a ruler and stopwatch. Write a precise number, not a guess.
04
Tape: attachment only
50cm of tape is ONLY for attaching the bungee to the bag. Cannot touch the egg or reinforce the bag. Violating this = Tier 2.
05
Use drop 1 as data
You get two drops. Don't try to win on drop 1 — observe carefully where the egg stops and adjust bands accordingly. Drop 2 should be your scored attempt.
06
Study the energy formulas
Assessment = 50 pts. Know GPE = mgh, KE = ½mv², EPE = ½kx². Know how they transform during the drop. The test happens while you build — review before you arrive.